## Slide 1: Diffusion-based Commuting Flow Generation for Fukuoka City: Adapting a Global OD Model for Sustainable Urban Mobility
New Context (Fukuoka city, Japan)
Local challenge: Fukuoka faces growing commuter flows between key centres (Hakata, Tenjin, Ohashi) with congestion, emissions
David Cheung
UCL MSc AI for Sustainable Development
Original Paper Generate commuting OD matrices using cheap, widely available data instead of expensive surveys/location traces.
Method: Treat each city as a directed weighted graph; use WeDAN diffusion model to generate edge weights from node attributes (Population, area, distances).
Results: On 3k+ US areas, graph-based generative models outperform gravity/radiation and pairwise ML on RMSE, NRMSE and CPC, and generalise across diverse urban/rural regions.
Adaptation of the Model Architecture
Base: Reuse the released OD diffusion model architecture (same number of layers / heads)
Context-specific changes: Bypass the GlODGen ArcGIS service and instead use predownloaded local WorldPop 2025 TIFs. For Fukuoka:
build a custom 431-cell grid from Japanese sub-ward polygons and calibrate cell-level population and area to official Fukuoka city totals.
tune diffusion sampling hyperparameters (T=250, DDIM_T_sample=25, sample_times=50) via Liverpool study.
Datasets Liverpool as baseline reproduction - GB_Liverpool shapefile (252 regions) and a GBR 2025 WorldPop TIF. Comparing result against the repo’s generation.npy OD matrix.
Fukuoka - a custom 431-cell grid, JPN 2025 WorldPop TIF, and calibration to Fukuoka’s official population (1,620,574) and area (343.39 km²). No ground-truth OD matrix is available, focus on structural plausibility.
Model Performance (Liverpool + transfer logic)
For Liverpool, I ran 10 seeds for each sample_times ∈ {5,10,20,50,80} and rescale generated OD to match total flows. The best setting is sample_times=50: RMSE ≈ 72.9 ± 1.8, NRMSE ≈ 0.99 ± 0.02, CPC ≈ 0.705 ± 0.006. Increasing beyond 50 gives marginal CPC gains for much higher runtime. I interpret this as a statistical reproduction of the reference matrix, not bitwise equality.
Evaluation of the Performance: Major CBD cells all lie within the top 1/3 of inflow/outflow ranks, consistent with Fukuoka’s known polycentric core. Quantile-banded flow networks show strong corridors from southern and western residential cells into central CBDs.
Email: ka.cheung.25@ucl.ac.uk
Github: https://github.com/kccheung/generate-od-pubtools
Goal: Use the OD generator to simulate realistic commuting flows over a grid of Fukuoka, supporting transport planning and low-carbon mobility policies, targeting SDG 11 (sustainable mobility) and SDG 10 (reduced inequalities)
City | Regions | Area (km²) | Population | OD Matrix Shape | Ground truth OD?
Liverpool | 252 | 111.8 | 508,961 | 252 × 252 | Yes (from original repository)
Fukuoka City | 431 | 343.39 | 1,620,574 | 431 × 431 | No (generated only)
For Fukuoka, without ground truth
- evaluate global structure:
Corr(pop, out_flow) = 0.895 and
Corr(pop, in_flow) = 0.852.
- commuting is strongly shaped by population, but not purely proportional, with multiple CBDs acting as both origins and destinations.
Discussion and Critical Reflections on SDGs
SDG 11 (Sustainable Cities): Help identify high-demand corridors where extra rail capacity or bus lanes and peripheral zones with weak connectivity to job centres.
SDG 10 (Reduced Inequalities): Cells with high outflow but weak local inflow suggest job-housing imbalances and potential transport poverty.